## Slide 1: Prototyping commercial IOT solutions with off the shelf hardware
Place amazon order on Monday present prototype on friday

## Slide 2: Who we Are
Will Murphy
  Cloud Engineer at Acuity Brands
  Focusing on Compute, Automation, and monitoring
Spence Kile
  Dev DBA at Acuity Brands
  Focusing on Data ingestion and Analytics

## Slide 3: Essential Skills
Some development/coding skills
  specific language not required
A little Creativity
Rubber Duck Debugging
  “Before you ask me, ask the duck”
  http://deviq.com/rubber-duck-debugging/

## Slide 4: Quick survey
Code background
  C#
  C\C++
  Python
  Other
OS Background
  Windows
  Linux
  “OS?!?, We don’t need no stinkin’ OS!”

## Slide 5: Problem statement
Commercial device
  Requires special hardware
  Requires special programming
  Requires expert setup
IoT compatibility for the device
  Secure data capture
  Data transformation capabilities
  Visibility into the Data captured

## Slide 6
INGESTION
PROCESSING
VISUALIZE
Stream Analytics
SENSORS
IoT Hub
Pi Zero W
Temperature
Humidity
Prototype Architecture
Pi 3 – GPIO
Temperature
Humidity
Pi 3 – Grove Pi
Temperature
Humidity
Sparkfun Thing
Temperature
Humidity
Power BI

## Slide 7: Hardware matrix
 | Pi Zero W | Pi 3 | Pi 3 GrovePi | Sparkfun Thing
Board | $10 | $35 | $35 | $16
Essentials | $22 | $8 | $8 | $0
Sensor & Wiring | $10 | $10 | $46 | $10
Total Investment | $42 | $53 | $89 | $26
Note:
These prices are based on using a single DHT11 sensor.
There are kits available for these platforms that can change the total investment and give you a broader range of sensors to use.

## Slide 8: Cloud Components
IoT Hub
  Free tier accepting 8k messages per day
    https://azure.microsoft.com/en-us/pricing/details/iot-hub/
  Device SDK available for C, .NET, Java, Node.js, and Python
    https://docs.microsoft.com/en-us/azure/iot-hub/iot-hub-devguide-sdks
Stream Analytics
  Simple analytics job to retrieve data, transform, and send to Power BI
  Similar to TSQL for job query
  Quick setup for prototyping
Power BI
  One GB per user quota limit
  10K rows/hour consumption limit for streaming data
Component | Price Per Month
IoT Hub | $0
Stream Analytics | $23
Power BI | $0

## Slide 9: DEMo

## Slide 10: Credits and additional information
This presentation and all the code samples at: atliotmay.murphymoments.com
GrovePi Starter Kit – Dexter Industries / Seeed Studio
BMP180 Windows Iot - Haris Sofos
Microsoft Azure IoT Starter Kit - SparkFun Thing